## Slide 1: Truck Driving Essentials
General Knowledge, Air Brakes,
Combination Vehicles,
Hazmat, Pre-Trip &
Post-Trip Inspections

## Slide 2: 1. General Knowledge 2. Air Brakes 3.Combination Vehicle 4. Hazardous Materials (Hazmat) 5. Tanker Endorsement 6. Pre-Trip, In-Route, and Post-Trip Inspections 7. Defensive Driving 8. Log Book (ELD) Rules & Regulations
TABLE OF
CONTENTS

## Slide 3: General Knowledge in Truck driving
Objectives:
Understand the fundamental principles of truck driving.
Learn industry regulations and safety practices.
Recognize key FMCSA rules and driver responsibilities.

## Slide 4: Introducing Truck driving
General knowledge in truck driving includes understanding fundamental driving concepts, industry regulations, safety practices, and the responsibilities of a commercial driver.
This knowledge is essential for ensuring safe and efficient transportation of goods while complying with legal and regulatory requirements.

## Slide 5: Types of Trucking Jobs
• Local Trucking – Short-distance deliveries, usually within a city or state.
• Regional Trucking – Transporting goods within a specific region, covering multiple states.
• Over-the-Road (OTR) Trucking – Long-distance transportation across the country.
• Hazmat Trucking – Specialized transportation of hazardous materials, requiring extra safety training.

## Slide 6: Basic Vehicle Controls
Driving a truck requires mastering basic vehicle controls to ensure safety and efficiency.
Steering: Always keep both hands on the wheel at the 9 and 3 o’clock positions to maintain full control. Avoid sudden steering movements, as trucks are large and heavy, making abrupt turns dangerous.
Braking: Trucks have multiple braking systems:
Service Brakes: Used during normal driving.

## Slide 7: Basic Vehicle Controls
Emergency Brakes: Engage when air pressure drops too low.
Parking Brakes: Used when the truck is stopped to prevent rolling.
Acceleration: Trucks take longer to speed up compared to regular vehicles. Gradual acceleration prevents cargo from shifting and maintains fuel efficiency.
Shifting Gears: Manual transmissions require smooth gear shifting to prevent transmission damage. Automatic trucks adjust gears automatically, but the driver should still monitor RPMs and road conditions.

## Slide 8: Basic Vehicle Controls
Emergency Brakes: Engage when air pressure drops too low.
Parking Brakes: Used when the truck is stopped to prevent rolling.
Acceleration: Trucks take longer to speed up compared to regular vehicles. Gradual acceleration prevents cargo from shifting and maintains fuel efficiency.
Shifting Gears: Manual transmissions require smooth gear shifting to prevent transmission damage. Automatic trucks adjust gears automatically, but the driver should still monitor RPMs and road conditions.

## Slide 9: Introducing Defensive Driving
Defensive driving techniques help prevent accidents and keep drivers safe.
Space Management:
Maintain at least 7-8 seconds following distance to allow for braking time.
Be extra cautious in heavy traffic, construction zones, or bad weather.
Looking Ahead:
Scan the road 12-15 seconds ahead to anticipate potential hazards.
Identify slow-moving vehicles, road debris, or sudden stops early.

## Slide 10: Introducing Defensive Driving
Blind Spots (“No-Zones”):
Trucks have large blind spots on the sides, rear, and front.
Avoid driving directly beside or behind another vehicle for long periods.
Lane Changes:
Use mirrors frequently and signal well in advance.
Change lanes gradually to avoid sudden movements.
Speed Control:
Adjust speed according to road, traffic, and weather conditions.
Avoid excessive speeds, especially on curves and downhill sections

## Slide 11: Understanding Road Signs & Rules
Understanding road signs and traffic laws is crucial for safe truck driving.
Regulatory Signs:
Speed limits, lane usage, weight restrictions, and truck routes must be obeyed.
Warning Signs:
Indicate curves, steep grades, narrow bridges, and construction zones.
Right of Way:
Always yield to emergency vehicles and pedestrians.
Understand four-way stop and intersection rules.
Railroad Crossings:
Always slow down and check for trains.
Stop 15-50 feet before tracks when required.

## Slide 12: Cargo Securement
Ensuring cargo is properly secured prevents accidents and damage.
Weight Limits:
Stay within legal weight limits for axles and overall gross weight.
Load Distribution:
Cargo must be evenly distributed to prevent shifting.
Tie Downs and Straps:
Use appropriate chains, straps, or tarps to keep loads stable.
Hazardous Materials (Hazmat):
Follow DOT regulations for labeling, placarding, and handling dangerous goods.

## Slide 13: Weather & Road Condition
Adjusting driving techniques for different weather conditions is essential.
Rain:
Increase following distance.
Avoid sudden braking to prevent skidding.
Snow/Ice:
Use tire chains when required.
Reduce speed and avoid sudden movements.
Fog:
Use low-beam headlights.
Drive at a slower speed for better reaction time.
High Winds:
Be cautious on bridges and open roads.

## Slide 14: Night Driving
Driving at night requires extra precautions.
Use High Beams Wisely:
Only when necessary; dim for oncoming traffic.
Clean Lights and Reflectors:
Keep headlights, taillights, and mirrors clean for maximum visibility.
Watch for Fatigue:
Take breaks every 2-3 hours.
Avoid driving if feeling drowsy.

## Slide 15: Night Driving
Driving at night requires extra precautions.
Use High Beams Wisely:
Only when necessary; dim for oncoming traffic.
Clean Lights and Reflectors:
Keep headlights, taillights, and mirrors clean for maximum visibility.
Watch for Fatigue:
Take breaks every 2-3 hours.
Avoid driving if feeling drowsy.

## Slide 16: Accident Procedures
If an accident occurs, follow these steps:
Stop Immediately – Move to a safe location if possible.
Secure the Scene – Use warning triangles or flares.
Call for Help – Contact law enforcement and emergency services.
Exchange Information – Share license, insurance, and contact details.

## Slide 17: Fuel Efficiency
Saving fuel reduces costs and environmental impact.
Idle Reduction: Turn off the engine when not in use.
Smooth Driving: Avoid rapid acceleration and braking.
Proper Tire Inflation: Maintain correct pressure to improve fuel economy.

## Slide 18: Communication on the Road
CB Radio: Useful for communicating road conditions with other truckers.
Hand Signals: Use when backing up with a spotter.

## Slide 19: Backing Up with a Spotter
Always agree on signals with the spotter before starting.
The spotter should stand where the driver can see them at all times.
If the driver loses sight of the spotter, they should stop immediately.
The spotter should use clear, exaggerated hand movements to avoid confusion.

## Slide 20: Parking and Backing
Backing Up: Always check mirrors and use a spotter if possible.
Docking: Align properly with loading docks.
Parking Brakes: Always engage when stopped.

## Slide 21: Industry Regulations
Truck drivers must comply with national and state regulations to ensure road safety and legal operation.
Weight Limits and Licensing:
- Understanding gross vehicle weight rating (GVWR) and axle weight limits.
- Obtaining the appropriate Commercial Driver’s License (CDL) classification.

## Slide 22: Industry Regulations
Commercial Driver’s License (CDL):
CDL Classes:
Class A: Required for operating combination vehicles with a GVWR of 26,001 lbs. or more, including tractor-trailers.
Class B: Required for single vehicles with a GVWR of 26,001 lbs or more, such as buses and dump trucks.
Class C: Required for vehicles transporting hazardous materials (HazMat) or passengers exceeding a specific limit.

## Slide 23: Industry Regulations
Endorsements:
T (Double/Triple Trailers): Required for hauling multiple trailers.
P (Passenger Transport): Required for buses carrying passengers.
N (Tanker Vehicles): Required for transporting liquid cargo.
H(Hazardous Materials):Required for transporting hazardous materials.
X (Combination of Tanker and HazMat): Required for hauling hazardous liquids.

## Slide 24: Industry Regulations
FMCSA and DOT Compliance:
Following rules set by the Federal Motor Carrier Safety Administration (FMCSA) and Department of Transportation (DOT).
Compliance with drug and alcohol testing regulations, medical examinations, and operational safety standards

## Slide 25: Industry Regulations
Road Signs:
Truck drivers must be able to read and interpret road signs to navigate safely.
Highway Signs:
Understanding regulatory, warning, and guide signs.
Recognizing speed limits, weight restrictions, and designated truck routes.
Special Truck-Related Signage:
Low clearance signs to prevent collisions with overpasses.
Weight limit postings for bridges and roads.
Hazardous material route designations.

## Slide 26: Industry Regulations
Safety Practices:
Truck drivers must adhere to strict safety measures to prevent accidents and ensure efficient transport.
Defensive Driving:
Anticipating potential hazards and reacting appropriately.
Keeping a safe following distance and managing blind spots.
Emergency Handling:
Recognizing and responding to tire blowouts, brake failures, and engine issues.
Using hazard signals and communicating with other road users in emergencies.
Avoiding Common Road Hazards:
Staying alert for sudden lane changes by other drivers.
Adjusting driving in adverse weather conditions such as rain, snow, and fog.

## Slide 27: Industry Regulations
Driver Responsibilities:
Truck drivers have essential duties beyond driving that contribute to overall safety and efficiency.
Maintaining Logbooks:
Keeping accurate records of driving hours using paper or electronic logs.
Ensuring compliance with Hours of Service (HOS) regulations to prevent driver fatigue.
Vehicle Inspections:
Conducting pre-trip, in-route, and post-trip inspections.
Checking tires, brakes, lights, fluid levels, and cargo securement before departure.

## Slide 28: Summary
This module covers
Fundamental truck driving concepts, including vehicle operation, industry regulations, road signs, and safety practices.
Provides an overview of FMCSA rules and driver responsibilities.

## Slide 29: Air brakes
Objectives:
Understand the air brake system and how it works.
Learn proper inspection procedures.
Identify common failures and preventive measures.

## Slide 30: Introducing Air brakes
Air brakes use compressed air to apply braking force in large vehicles. They are a critical component in heavy-duty vehicles, utilizing compressed air to activate the braking mechanism. This system is favored in commercial trucks due to its reliability and ability to maintain braking power even with minor leaks.
Understanding their function, components, and maintenance is critical for safe operation and regulatory compliance.

## Slide 31: How Air Brakes Function
Air brake systems are used in large commercial vehicles due to their reliability and effectiveness.
The system relies on compressed air instead of hydraulic fluid to activate the brakes.

## Slide 32: Key Components & Their Functions
Air Compressor
Function: Generates and supplies compressed air to the brake system.
Operation: Typically engine-driven, ensuring a continuous supply of air.
Maintenance Example: Regularly inspect for oil leaks and ensure the compressor is building pressure within the manufacturer's specified time frame.
Air Storage Tanks (Reservoirs)
Function: Store compressed air for immediate use during braking.
Safety Feature: Equipped with drain valves to remove accumulated moisture and oil.
Maintenance Example: Drain the tanks daily to prevent water accumulation, especially in humid conditions, to avoid brake failure due to freezing.

## Slide 33: Key Components & Their Functions
Brake Chambers
Function: Convert air pressure into mechanical force to apply the brakes.
Operation: Air pressure pushes a diaphragm, moving the pushrod to engage the brakes.
Inspection Example: Check for audible air leaks around the chamber and ensure the pushrod moves freely without obstruction.
Slack Adjusters and Pushrods
Function: Maintain the correct distance between brake shoes and drums, ensuring effective braking.
Adjustment Example: During inspections, pull the slack adjuster by hand; it should not move more than approximately one inch. Excessive movement indicates the need for adjustment.

## Slide 34: Key Components & Their Functions
Brake Shoes and Drums
Function: Create the friction necessary to slow down or stop the vehicle.
Wear Indicator Example: Regularly inspect brake shoes for wear; thin linings can lead to reduced braking efficiency and should be replaced promptly.
Service Brakes:
Activated by the foot pedal, applying pressure to slow or stop the vehicle.

## Slide 35: Key Components & Their Functions
Emergency Brakes:
Engaged automatically when air pressure drops below a safe level.
Spring Brakes:
Use a large coil spring to hold brakes in place when parking or during emergency stops.

## Slide 36: Inspection Procedure
Regular inspections ensure that air brake systems function correctly and prevent dangerous failures.
Pre-Trip Inspection:
Check air compressor operation and reservoir pressure levels.
Inspect hoses and lines for leaks, cracks, or wear.
Test brake application to ensure proper response.
In-Route Inspection:
Monitor air pressure gauge to ensure it stays within the normal range (typically 90-120 PSI).
Listen for air leaks and check for unusual braking response.
Ensure proper function of emergency and parking brakes

## Slide 37: Air Brake Test
A CDL holder must be able to conduct an air brake test to verify system performance.
Performing the Leak Rate Test:
Fully charge the air system and turn off the engine.
Release the parking brake and monitor the air pressure drop (should not exceed 3 PSI per minute in a single vehicle or 4 PSI per minute in a combination vehicle).
Understanding Low Air Pressure Warning Systems:
Vehicles are equipped with a warning signal (light or buzzer) that activates when pressure drops below 60 PSI.
Spring brakes engage automatically if pressure falls below 20-45 PSI.

## Slide 38: Preventing Failures
Proper maintenance and correct braking techniques help prevent air brake failures.
Regular Maintenance:
Drain air tanks daily to remove moisture and prevent freezing.
Replace worn-out hoses and fittings to prevent leaks.
Ensure air dryers function properly to reduce moisture in the system.
Proper Braking Techniques:
Avoid excessive braking to prevent overheating and brake fade.
Use controlled braking or stab braking techniques when necessary.
Keep a safe following distance to reduce the need for sudden stops.

## Slide 39: Air Brake System Operation
Applying the Brakes: Pressing the brake pedal increases air pressure in the brake chambers, pushing the diaphragm and activating the brakes.
Releasing the Brakes: Releasing the pedal decreases air pressure, allowing return springs to disengage the brakes.
Emergency Braking: In case of significant air loss, spring brakes automatically engage to stop the vehicle.

## Slide 40: Summary
In-depth training on air brake systems, including how they function, how to inspect them,
how to prevent failures.
Covers the air brake test required for CDL holder

## Slide 41: Combination Vehicles
Objectives:
Learn about tractor-trailers and their operation.
Understand coupling and uncoupling procedures.
Recognize weight distribution and handling challenges

## Slide 42: Introducing Combination Vehicles
Combination vehicles include trucks with trailers, such as tractor-trailers.
These vehicles require special handling due to their size and articulation, making it essential for drivers to understand proper operation, weight distribution, and safety procedures.

## Slide 43: Coupling & Uncoupling Procedures
Proper coupling and uncoupling of tractor-trailers are vital for safe operations. Incorrect procedures can lead to accidents, equipment damage, or cargo loss.

## Slide 44: Coupling Procedure
1. Inspect Fifth Wheel:
Ensure the fifth wheel is securely mounted, undamaged, and properly lubricated. Verify that the jaws are open and the locking mechanism is functional.
2. Inspect Trailer Kingpin and Area:
Check the trailer kingpin for damage or excessive wear. Ensure the area around the trailer is clear of obstacles.
3. Position Tractor:
Align the tractor directly in front of the trailer. Back up slowly, centering the kingpin with the fifth wheel. Stop just before contact.

## Slide 45: Coupling Procedure
4. Secure Trailer:
Engage the trailer brakes to prevent movement during coupling.
5. Back Under Trailer:
Using the lowest reverse gear, back the tractor slowly under the trailer to avoid hitting the kingpin too hard. Stop when the kingpin is locked into the fifth wheel.
6. Check Connection Security:
Perform a tug test by gently pulling forward with the trailer brakes engaged to ensure the fifth wheel jaws have locked onto the kingpin securely.

## Slide 46: Coupling Procedure
7. Connect Air and Electrical Lines:
Attach the service and emergency air lines and the electrical cable between the tractor and trailer. Ensure all connections are secure and free from damage.
8. Raise Landing Gear:
Fully retract the landing gear to prevent damage during transit.
9. Final Inspection:
Walk around the vehicle to verify all connections are secure, lights are functioning, and there are no visible issues

## Slide 47: Uncoupling Procedure
1. Position Vehicle:
Park on level ground and apply both tractor and trailer parking brakes.
2. Lower Landing Gear:
Extend the landing gear until it makes firm contact with the ground. In low gear, turn the crank a few extra times to lift some weight off the tractor.
3. Disconnect Air and Electrical Lines:
Detach the air lines and electrical cable, securing them to the tractor to prevent damage.

## Slide 48: Uncoupling Procedure
4. Unlock Fifth Wheel:
Pull the fifth wheel release handle to disengage the locking mechanism.
5. Pull Tractor Forward:
Slowly move the tractor forward until the fifth wheel is clear of the trailer kingpin.
6. Secure Tractor:
Apply the tractor parking brake and conduct a final inspection to ensure the trailer is stable and the area is clear.

## Slide 49: Weight Distribution
Proper weight distribution is essential for maintaining vehicle stability and control.
Load Balancing:
Evenly distribute weight across axles to prevent overloading.
Ensure cargo is secured to prevent shifting during transit.
Effects on Braking and Stability:
Poorly distributed weight can cause uneven braking and loss of control.
Overloaded axles can lead to mechanical failures and regulatory violations.

## Slide 50: Handling Challenges
Due to their size, combination vehicles have unique handling difficulties that drivers must account for.
Wider Turns:
Trucks with trailers require extra space when making turns.
Drivers must swing wide to avoid hitting curbs or obstacles.
Longer Stopping Distances:
Heavier loads require more time and distance to come to a complete stop.
Drivers should maintain safe following distances and anticipate stops in advance.
Backing Up with a Trailer:
Trailer pivoting makes reversing more challenging.
Small steering adjustments are necessary to control trailer direction.

## Slide 51: Jackknife Prevention
Jackknifing occurs when the trailer swings too far to one side, creating a sharp angle with the tractor. It can lead to loss of control and serious accidents.
Understanding Trailer Swing:
Rapid braking or sudden steering can cause the trailer to swing uncontrollably.
Drivers should avoid harsh braking, especially on wet or slippery roads.
Skid Control Techniques:
Reduce speed before making turns to prevent skidding.
Gradually apply brakes instead of slamming them to maintain stability

## Slide 52: Safety Tips
Consistency: Always follow a standardized procedure to minimize errors.
Awareness: Be mindful of your surroundings, especially in crowded or confined spaces.
Training: Regularly review and practice coupling and uncoupling techniques to maintain proficiency.

## Slide 53: Summary
Training on tractor-trailers and other combination vehicles.
Covers coupling and uncoupling procedures, weight distribution,
Covers handling challenges unique to these vehicles.
Safety Tips

## Slide 54: Hamzat
Objectives
Understand HazMat regulations and safety measures.
Learn how to handle and transport hazardous materials.
Identify emergency response procedures

## Slide 55: Introducing Hamzat
Hazmat stands for Hazardous Materials, which are substances that can pose a risk to health, safety, and the environment.
Truck drivers must undergo special training and certification to transport hazmat safely.

## Slide 56: Classes of Hamzat
.
Class | Hazmat Type | Examples
1 | Explosives | Fireworks, Ammunition
2 | Gases | Propane, Oxygen Tanks
3 | Flammable Liquids | Gasoline, Diesel, Paint Thinners
4 | Flammable Solids | Matches, Magnesium
5 | Oxidizing Substances | Bleach, Hydrogen Peroxide
6 | Toxic & Infectious Substances | Pesticides, Medical Waste
7 | Radioactive Materials | Uranium, Nuclear Medicine
8 | Corrosive Substances | Battery Acid, Drain Cleaner
9 | Miscellaneous Dangerous Goods | Lithium Batteries, Dry Ice

## Slide 57: Rules for Transporting Hazmat Loads
1. Hazmat Endorsement – Drivers must pass a Hazmat Endorsement Test to obtain a special license.
2. Proper Labeling – All hazmat shipments must have correct labels and placards on the truck.
3. Securing the Load – Hazardous materials must be properly secured to prevent leaks or spills.
4. Emergency Response Plan – Drivers must know what to do in case of an accident involving hazmat.
5. Route Restrictions – Some roads and tunnels restrict hazmat transport, requiring drivers to plan alternative routes.
6. Documentation – Truckers must carry proper paperwork, including a Material Safety Data Sheet (MSDS), with details about the hazardous cargo.
7. Regular Vehicle Inspections – Hazmat trucks must be in top condition to prevent accidents.

## Slide 58: Hazardous Materials (HazMat) Endorsement
The HazMat endorsement allows commercial drivers to transport hazardous substances safely.
Drivers must follow strict federal regulations to ensure public safety and environmental protection.

## Slide 59: Labeling and Handling
Proper labeling and handling of hazardous materials ensure safety and compliance with federal regulations.
Marking and Labeling:
Understanding DOT-required placards and labels.
Identifying hazard classes such as flammable, toxic, and corrosive materials.
Packaging and Securement:
Ensuring proper container usage for different hazardous substances.
Using correct tie-downs and storage techniques to prevent leaks and spills.

## Slide 60: Emergency Response
Being prepared for hazardous material incidents is crucial for safety.
Handling Spills and Leaks:
Following emergency action plans to contain and clean up spills.
Understanding first-aid procedures in case of exposure.
Using absorbent materials and spill containment barriers to prevent environmental damage.
Fire and Explosion Response:
Knowing which fire extinguishers to use for specific hazardous materials.
Evacuation procedures and notifying emergency responders.
Identifying potential ignition sources and mitigating risks in case of a fire.

## Slide 61: Emergency Equipment & Protocols
Carrying emergency response kits, including protective gear, absorbent materials, and neutralizing agents.
Using the Emergency Response Guidebook (ERG) to identify the correct procedures for different types of hazardous materials.
Coordinating with first responders and law enforcement to ensure proper containment and public safety measures.
Incident Reporting:
Understanding the importance of immediate reporting to the proper authorities, including DOT and local emergency services.
Maintaining accurate records of incidents and corrective actions taken.
Cooperating with investigations and follow-up measures to prevent future incidents.

## Slide 62: Endorsement Requirements
To obtain a HazMat endorsement, drivers must meet federal requirements.
TSA Background Checks:
Passing a security threat assessment from the Transportation Security Administration (TSA).
Submitting fingerprints and personal information for clearance.
Written Exam:
Covering hazardous material classifications, safe transport, and emergency response.
Studying the Hazardous Materials Regulations (HMR) handbook.

## Slide 63: Regulatory Compliance
Compliance with DOT and FMCSA regulations is essential for legally transporting hazardous materials.
Transport Restrictions:
Understanding restricted routes and prohibited materials.
Following load limits and segregation rules for different hazard classes.
Documentation Requirements:
Maintaining proper shipping papers, manifests, and emergency contact details.
Ensuring all paperwork is accessible to authorities during inspections

## Slide 64: Summary
Provides knowledge on
Hamzat
Classes of Hamzat
Rules for transporting Hamzat
Safe transportation of hazardous materials, including labeling, handling, emergency response
HazMat endorsement requirements

## Slide 65: Tankers Endorsement
Objectives
Understand the challenges of transporting liquid cargo.
Learn about load surge and weight shifting.
Master safe braking techniques for tankers.
Comprehend regulatory requirements for liquid transport.

## Slide 66: Introducing Tanker Endorsement
The tanker endorsement is required for commercial drivers transporting liquid cargo.
Liquid loads behave differently than solid freight, affecting vehicle handling and stability.

## Slide 67: Load Surge Effects
Liquid cargo movement significantly impacts a vehicle’s stability and control.
Understanding Load Surge:
Liquid cargo moves back and forth inside the tank when braking, accelerating, or turning.
The surge can cause the truck to lurch forward or backward, making it harder to stop or accelerate smoothly.
Managing Load Surge:
Using smooth and gradual acceleration and braking to reduce movement.
Ensuring proper baffling inside the tanker to limit liquid flow.

## Slide 68: Weight Shifting
Weight shifting occurs when liquid cargo moves unpredictably, affecting balance.
Center of Gravity Considerations:
Liquid cargo can shift side to side, increasing the risk of rollovers.
Tanker trucks have a higher center of gravity, making turns more dangerous.
Adjusting Driving for Stability:
Slowing down before curves and turns.
Keeping a steady speed to minimize the risk of cargo sloshing and shifting.

## Slide 69: Braking Techniques
Proper braking techniques help prevent cargo shifts and maintain control.
Gradual Braking:
Abrupt braking can cause liquid to surge forward, leading to loss of control.
Using controlled, progressive braking to maintain stability.
Stopping Distance Considerations:
Tankers require longer stopping distances due to weight and liquid motion.
Anticipating traffic changes and maintaining a safe following distance.

## Slide 70: Regulatory Requirements
Transporting liquid cargo is subject to strict federal and state regulations.
Types of Liquid Cargo:
Fuel Transport: Requires additional hazardous materials (HazMat) endorsement.
Chemical Transport: Must follow environmental safety regulations.
Food-Grade Liquids: Must comply with sanitation and contamination prevention rules.
Federal Compliance:
Following DOT and FMCSA regulations on tanker truck operation.
Adhering to load weight limits and transportation routes.
Inspection and Maintenance:
Conducting pre-trip and post-trip inspections to ensure tank integrity.
Checking for leaks, valve security, and pressure systems before transportation

## Slide 71: Summary
Covers safe transportation of liquid cargo, including
load surge effects
weight shifting
proper braking techniques
regulatory requirements
Essential for fuel, chemical, and food-grade liquid transport

## Slide 72: Pre-Trip , In-Route, & Post-Trip Inspections
Objectives
Learn the importance of inspections for safety and compliance.
Understand pre-trip, in-route, and post-trip inspection procedures.
Identify critical inspection points to prevent breakdowns and violations

## Slide 73: Introducing Pre-trip, in-route, & post-trip inspections
Pre-trip, in-route, and post-trip inspections are essential
procedures that ensure a commercial vehicle is safe and compliant with federal regulations.
These inspections help identify mechanical issues before they lead to accidents or costly repairs.

## Slide 74: What is a Pre-trip Inspection
A pre-trip inspection is a mandatory vehicle check before starting a trip to ensure the truck is safe and roadworthy. The inspection prevents mechanical failures and ensures compliance with Department of Transportation (DOT) regulations.

## Slide 75: Steps for a Proper Pre-Trip Inspection
A thorough pre-trip inspection ensures the vehicle is roadworthy before starting a journey.
Exterior Inspection:
Check tire pressure, tread depth, and signs of wear or damage.
Inspect brakes, including air brake pressure levels and leaks.
Test headlights, brake lights, turn signals, and reflective markers.
Engine Compartment:
Verify fluid levels (oil, coolant, transmission, power steering, and windshield washer fluid).
Check belts and hoses for cracks, leaks, or loose fittings.
Inspect battery connections and ensure they are secure.
Cab Inspection:
Confirm dashboard warning lights are off and gauges are functioning.
Test windshield wipers, defrost, and climate control.
Check mirrors and adjust them for proper visibility.
Cargo Securement:
Ensure cargo is properly loaded and secured to prevent shifting.
Confirm trailer coupling is locked and safety chains are in place.

## Slide 76: Why is a pre-trip Important?
• Ensures safety by preventing breakdowns.
• Helps drivers comply with DOT regulations.
• Saves money by reducing costly repairs.
• Prevents accidents due to mechanical failures.

## Slide 77: What is a In-Route Inspection
During a trip, periodic checks help detect potential issues before they escalate.
- *Monitoring Vehicle Performance:*
- Keep an eye on gauges for engine temperature, oil pressure, and battery voltage.
- Listen for unusual noises or vibrations that indicate mechanical issues.
- *Brake and Tire Checks:*
- Stop periodically to inspect brake function and air pressure levels.
- Check tire condition and pressure to avoid blowouts.
- *Cargo and Load Securement:*
- Ensure tie-downs and straps remain tight.
- Confirm hazardous material placards are visible and in place.
- *Weather and Road Conditions:*
- Adjust driving based on weather conditions (rain, snow, ice).
- Be prepared to pull over if conditions become unsafe

## Slide 78: In-Route Inspection
During a trip, periodic checks help detect potential issues before they escalate.
- *Monitoring Vehicle Performance:*
- Keep an eye on gauges for engine temperature, oil pressure, and battery voltage.
- Listen for unusual noises or vibrations that indicate mechanical issues.
- *Brake and Tire Checks:*
- Stop periodically to inspect brake function and air pressure levels.
- Check tire condition and pressure to avoid blowouts.
- *Cargo and Load Securement:*
- Ensure tie-downs and straps remain tight.
- Confirm hazardous material placards are visible and in place.
- *Weather and Road Conditions:*
- Adjust driving based on weather conditions (rain, snow, ice).
- Be prepared to pull over if conditions become unsafe

## Slide 79: What is a post-trip Inspection?
A post-trip inspection is performed after completing a trip to identify any mechanical issues that need fixing before the next trip.

## Slide 80: Key Steps in a Post-Trip Inspection
After completing a trip, an inspection helps identify any maintenance needs.
Final Walk around Check:
Inspect tires, brakes, and lights for any new damage or issues.
Ensure no leaks have developed from the engine or fuel system.
Reporting and Documentation:
Complete a Driver Vehicle Inspection Report (DVIR).
Report any mechanical defects to maintenance personnel immediately.
Note any issues that need attention before the next trip.

## Slide 81: Summary
Teaches drivers how to properly inspect a truck before, during, and after a trip to ensure roadworthiness.
Covers checking tires, brakes, lights, fluid levels, and cargo securement

## Slide 82: Defensive Driving
Objectives
Understand the principles of defensive driving.
Learn techniques to prevent accidents.
Adapt to changing road conditions and hazards.

## Slide 83: Introducing Defensive Driving
Defensive driving involves anticipating road hazards, maintaining control in unpredictable situations, and taking proactive measures to prevent accidents.
This approach helps drivers stay safe and reduce risks on the road.

## Slide 84: Hazard Awareness
Recognizing potential hazards on the road helps drivers prepare and react appropriately.
Identifying Common Hazards:
Weather conditions such as rain, snow, fog, and ice that reduce visibility and traction.
Road conditions like potholes, debris, and construction zones that require cautious navigation.
Pedestrians, cyclists, and motorcyclists who may be unpredictable in traffic.
Recognizing Aggressive Drivers:
Signs include tailgating, excessive lane changing, and speeding.
Strategies for dealing with aggressive drivers include staying calm, avoiding confrontations, and giving them space.
Monitoring Traffic Flow:
Watching for sudden stops, merging vehicles, and unexpected lane changes.
Using scanning techniques to assess surroundings, including checking intersections and blind spots.

## Slide 85: Accident Prevention
Taking proactive steps to reduce the risk of collisions is essential for defensive driving.
Maintaining Safe Following Distances:
Using the "three-second rule" to ensure enough stopping distance between vehicles.
Increasing following distance in bad weather or heavy traffic.
Staying Alert and Focused:
Avoiding distractions such as mobile phones, eating, or adjusting controls while driving.
Recognizing signs of driver fatigue and taking breaks when needed.
Anticipating Other Drivers’ Actions:
Watching for signals, brake lights, and lane movements to predict behavior.
Being prepared for sudden stops or reckless maneuvers by other drivers.

## Slide 86: Managing Blind Spots
Blind spots are areas around a vehicle that cannot be seen using mirrors alone, making them a common cause of accidents.
Using Mirrors Effectively:
Adjusting side and rearview mirrors properly to minimize blind spots.
Checking mirrors frequently, especially before changing lanes or merging.
Performing Head Checks:
Looking over the shoulder before making turns or lane changes.
Ensuring there are no vehicles or motorcycles in blind spots before maneuvering.
Avoiding Other Vehicles’ Blind Spots:
Staying out of the "No-Zone" areas of large trucks where drivers have limited visibility.
Moving ahead or slowing down if caught in another vehicle’s blind spot.

## Slide 87: Avoiding Aggressive Driving
Aggressive driving behaviors increase the risk of accidents and road rage incidents.
Maintaining Patience and Self-Control:
Avoiding emotional reactions to rude or reckless drivers.
Focusing on safe driving rather than retaliating or engaging with aggressive drivers.
Obeying Speed Limits:
Adhering to posted speed limits to maintain control and reaction time.
Reducing speed in hazardous conditions, such as fog, rain, or heavy traffic.
Yielding the Right of Way:
Following traffic rules at intersections, merging lanes, and pedestrian crossings.
Allowing faster-moving vehicles to pass rather than blocking lanes.

## Slide 88: Summary
This lesson focuses on
Hazard awareness
Accident prevention
Adapting to road conditions.
Strategies for maintaining safe following distances which are:
Managing blind spots
Avoiding aggressive driving.

## Slide 89: Log Book (ELD) Rules & Regulations
Objectives
Understand FMCSA HOS regulations.
Learn how to record duty status using ELDs.
Recognize penalties for logbook violations.
Understand the functionality and benefits of ELDs.

## Slide 90: Introducing ELDs
Electronic Logging Devices (ELDs) are digital systems that automatically record a driver's Hours of Service (HOS) to ensure compliance with Federal Motor Carrier Safety Administration (FMCSA) regulations.
They replace traditional paper logbooks and help prevent violations related to excessive driving hours.

## Slide 91: Components of ELDs
ELDs are designed to track and log a driver’s hours automatically, improving accuracy and compliance.
We have different components of ELDs.
In this module, we will focus on 4 types namely:
1. Hours of Service (HOS) Regulations
2. Electronic Logging Devices (ELDs)
3. Duty Status Recording
4. Rest Break Requirements

## Slide 92: Hours of Service (HOS) Regulations
HOS regulations are designed to prevent driver fatigue and ensure road safety.
Daily and Weekly Driving Limits:
Maximum of 11 hours of driving after 10 consecutive off-duty hours.
Maximum of 14 consecutive hours on duty, including driving and breaks.
Mandatory 30-minute rest break after 8 hours of driving.
Maximum of 60 hours on duty in 7 days or 70 hours in 8 days.
On-Duty vs. Off-Duty Time:
Off-duty time includes rest, meals, and personal activities.
On-duty time includes driving, fueling, loading/unloading, and vehicle inspections.

## Slide 93: Functionality of ELDs
Syncs with the vehicle’s engine to record driving time automatically.
Tracks duty status (driving, on-duty not driving, off-duty, and sleeper berth).
Stores data securely and allows roadside inspection access.

## Slide 94: Benefits of ELDs
Reduces paperwork and human errors in logging hours.
Prevents HOS violations by providing real-time tracking.
Enhances safety by reducing driver fatigue.
Helps fleet managers monitor and optimize operations.

## Slide 95: Duty Status Recording
Drivers must accurately log their duty status using ELDs.
Types of Duty Status:
Off-Duty: Not working, including rest breaks and personal time.
Sleeper Berth: Resting in the truck’s sleeping compartment.
Driving: When the vehicle is in motion.
On-Duty (Not Driving):Working but not driving (e.g., inspections, fueling, loading/unloading).
Automatic Data Capturing:
ELDs record driving time automatically when the vehicle is in motion.
Drivers must manually change duty status when switching to off-duty or sleeper berth.

## Slide 96: Rest Break Requirements
Drivers must comply with rest break rules to maintain alertness and safety.
Mandatory Rest Periods:
A 30-minute break is required after 8 consecutive hours of driving.
Drivers must take 10 consecutive off-duty hours before starting a new driving period.
Split sleeper berth provisions allow drivers to divide their rest periods under specific conditions.

## Slide 97: Importance of Rest Breaks
Helps reduce fatigue-related accidents.
Ensures drivers maintain focus and reaction time.

## Slide 98: Penalties for Violations
Non-compliance with ELD and HOS regulations can result in serious penalties.
Types of Violations:
Exceeding daily or weekly driving limits.
Falsifying logs or tampering with ELDs.
Failure to have an ELD (for applicable drivers).

## Slide 99: Consequences of Non-compliance
Fines ranging from hundreds to thousands of dollars per violation.
Placing drivers or vehicles out of service.
Impact on the carrier’s safety rating and increased DOT audits

## Slide 100: Summary
Explains FMCSA Hours of Service (HOS) regulations
How to record duty status using Electronic Logging Devices (ELDs).
Covers rest break requirements and penalties for violations.