## Slide 1: Air Brake Handout
For safe driving

## Slide 2: Table Of Contents
1. Introduction to Air Brakes
2. Components of Air Brakes
3. How Air Brakes Work
4. Pre-Trip Inspection
5. Post –Trip Inspection
6. Emergency Procedures

## Slide 3: Introduction to Air Brakes
Air brakes are a critical safety system or type of braking system used in heavy vehicles like trucks, buses, and trailers. They use compressed air to apply pressure to the brake pads or shoes, slowing or stopping the vehicle.
Air brakes are fundamentally different from car brakes. Instead of brake fluid, they use compressed air, making them ideal for large vehicles. The big safety advantage? If air pressure drops too low, the spring brakes automatically engage to stop the vehicle.
Whether you drive a truck, bus, forklift, or car with air brakes, understanding the system keeps you and others safe.

## Slide 4: Introduction to Air Brakes
Advantages of Air Brakes:
✔ More reliable for heavy loads (trucks, buses, trailers).
✔ Less prone to failure due to leaks (compared to hydraulic systems)
✔ Better heat dissipation
✔ Works even with minor leaks
✔ Safer—brakes engage if air pressure is lost (spring brakes).
✔ More durable for frequent stopping (BRT, school buses).
✔ Works in extreme conditions (better than hydraulic brakes in heat/cold).

## Slide 5: Quiz
❓What happens if air pressure gets too low in an air brake system?
A) Brakes become more sensitive
B) Spring brakes automatically engage ✅
C) The vehicle speeds up

## Slide 6: Types of Vehicles Using Air Brake
Summary
Vehicle Type | Why Air Brakes | Special Notes
Trucks & Trailers | Heavy loads, long stopping distance | Must pass CDL air brake test
School Buses | Safety for children, frequent stops | Daily air tank draining required
BRT (Bus Rapid Transit) | High passenger capacity, quick stops | Frequent brake checks needed
Forklifts (Some Models) | Heavy lifting, stability control | Often have combined hydraulic/air systems
Some Luxury Cars (e.g., Mercedes) | Enhanced braking performance | Rare, but used in high-performance models

## Slide 7: Main Components of an Air Brake System
Think of the air compressor as the heart of the system—it keeps the tanks pressurized. The slack adjusters are like the 'calibration' for your brakes; if they're misadjusted, your brakes won’t work efficiently.
Air brake Components
1. Air Compressor – Pumps air into the system.
2. Air Reservoirs (Tanks) – Store compressed air for braking(100-120 psi).
3. Brake Pedal (Foot Valve) – Controls air flow to apply brakes.
4. Brake Chambers – Convert air pressure into mechanical force.
5. Slack Adjusters – Maintain proper brake shoe clearance.
6. Brake Drums & Shoes (or Disc Brakes) – Create friction to stop the vehicle.
7. Safety Valves – Prevent over-pressurization.
8. Drain Valves – Remove moisture from air tanks.

## Slide 8: Quiz
❓ Which component ensures brake shoes stay at the right distance from drums?
A) Air compressor
B) Slack adjuster ✅
C) Foot valve

## Slide 9: How Air Brakes Work
Air brakes do not work like car brakes—they require air pressure to release the brakes (spring brakes engage when air pressure is low).
Unlike car brakes, where pressing the pedal applies braking force, in air brakes, pressing the pedal releases air to activate the brakes. This is why losing air pressure is dangerous—the brakes can lock up!
⚠Critical Difference from Car Brakes:
Air brakes need air pressure to release brakes (spring brakes lock if air is lost).
Hydraulic brakes (in cars) need fluid pressure to apply brakes
Key Points:
1. Compression – The air compressor fills the reservoirs with compressed air.
2. Application – Pressing the brake pedal releases air into the brake chambers.
3. Activation – The chambers push the slack adjusters, forcing brake shoes against drums.
4. Release – Releasing the pedal exhausts air, releasing the brakes.

## Slide 10: Quiz
❓ What is the key difference between air brakes and car brakes?
A) Air brakes use hydraulic fluid
B) Air brakes require air pressure to release brakes ✅
C) Air brakes only work in cold weather

## Slide 11: Pre-Trip Inspection
A proper pre-trip inspection can mean the difference between a safe journey and a brake failure. Always listen for air leaks—hissing sounds mean trouble
Pre-Trip Air Brake Checks (All Drivers)
✅ Check Air Compressor – Listen for proper operation.
✅ Check Air Pressure Gauge – Must be 90-120 psi before driving.
✅ Listen for Air Leaks – Hissing = problem.
✅ Inspect Air Lines & Hoses – No cracks or leaks
✅ Test Low Air Warning – Buzz/Alarm/light at 60 psi.
✅ Drain Air Tanks – Water buildup causes rust & failure i.e. Remove moisture daily.
✅ Check/Tug Slack Adjusters – Should not move more than 1 inch when pulled.
✅ Perform a Brake Test – Check stopping power before moving

## Slide 12: Quiz
❓What should you do if you hear a hissing sound during a pre-trip check?
A) Ignore it—it’s normal
B) Tighten fittings or replace damaged hoses ✅
C) Drive faster to compensate

## Slide 13: Post-Trip Inspection
Think of post-trip inspections like brushing your teeth—skip it, and problems will grow. A 5-minute check today can prevent a roadside breakdown tomorrow
Step-by-Step Post-Trip Air Brake Inspection
1. Park Safely & Secure the Vehicle
✔ Set parking brakes (spring brakes engaged).
✔ Chock wheels if on an incline.
✔ Turn off the engine but keep air pressure for checks.
2. Drain Air Tanks (Critical!)
✔ Locate drain valves on all air tanks (usually at the bottom).
✔ Open valves fully to release moisture & contaminants.
✔ Listen for air/water mix – If only air comes out, tanks may be too dry (check for leaks).
💡 Pro Tip: Draining daily prevents rust, frozen lines in winter, and brake failure.

## Slide 14: Post-Trip Inspection
3. Check for Air Leaks
✔ Listen for hissing sounds (sign of leaks in hoses, fittings, or chambers).
✔ Inspect air lines for cracks, abrasions, or loose connections.
✔ Test with soapy water if a leak is suspected (bubbles will form).
4. Inspect Brake Components
✔ Slack adjusters – Should not move more than 1 inch when pulled.
✔ Brake chambers – Check for cracks, dents, or air leaks.
✔ Brake drums/shoes – Look for excessive wear, grease, or overheating (blue discoloration = overheating).

## Slide 15: Post-Trip Inspection
5. Verify Air Pressure Build-Up
✔ Start the engine and observe the air pressure gauge.
✔ Should build to 100-125 psi within 3 minutes (varies by vehicle).
✔ If slow to build: Possible compressor or belt issue.
6. Test Parking/Emergency Brakes
✔ Release the parking brake and attempt to drive slowly.
✔ Engage parking brake – Wheels should lock immediately.
✔ If weak: May indicate a faulty spring brake or air leak.
7. Document & Report Issues
✔ Note any leaks, unusual noises, or pressure problems.
✔ Report defects to maintenance immediately.

## Slide 16: Post-Trip Inspection
Why Post-Trip Inspections Matter
- Prevents moisture buildup (causes rust & brake failure).
- Catches small leaks before they become major failures.
- Ensures next driver starts with a safe system
- FMCSA/DOT Compliance – Required for commercial vehicles.

## Slide 17: Common Air Brake Problems & Solutions
Summary
Problem | Possible Cause | Solution
Slow pressure build-up | Compressor failure, leaks | Check belts, hoses, repair leaks
Air leaks (hissing sound) | Cracked hoses, loose fittings | Tighten or replace parts
Brakes not releasing | Frozen brake chamber, stuck valve | Inspect & replace faulty parts
Excessive brake wear | Misadjusted slack adjusters | Adjust or replace

## Slide 18: Quiz
❓ How often should you drain air tanks?
A) Weekly
B) Only in winter
C) After every shift ✅
❓ What does a hissing sound usually indicate?
A) Normal operation
B) An air leak ✅
C) High fuel efficiency
❓ How much should slack adjusters move when pulled?
A) Less than 1 inch ✅
B) 3 inches
C) Doesn’t matter

## Slide 19: Emergency Braking & Stopping Distance
Each vehicle has unique needs. Bus drivers, for example, must brake smoothly to avoid throwing passengers around. Forklift operators? Never park without engaging the spring brake—it’s a safety must!
Key Points:
Air brakes take longer to stop than hydraulic brakes.
Stopping distance increases with speed, weight, and road conditions.
Use controlled braking (avoid locking wheels).
If brakes fail, use the emergency (spring) brake or downshift.

## Slide 20: Emergency Braking & Stopping Distance
If your brakes fail, don’t panic! Pumping the pedal might rebuild enough pressure to stop. If not, the spring brakes will kick in—but they’re a last resort, so use them wisely.
Emergency Procedures for Air Brake Failure
1. Pump the Brake Pedal – May rebuild air pressure.
2. Use Spring Brakes (Emergency Brake) – Activates automatically if pressure drops too low.
3. Downshift (Manual Transmission) – Engine braking helps slow the vehicle.
4. Find a Safe Escape Path – Avoid steep hills if brakes fail.

## Slide 21: Emergency Braking & Stopping Distance
Special Tips for Different Drivers
🚗 Car Drivers (Rare Air Brake Systems)
- Some high-end cars use air-assisted brakes.
- If your car has air brakes, check pressure regularly.
🚛 Truck & Trailer Drivers
- Never ignore the low-air warning!
- Double-check trailer brake connections.
🚌 School Bus & BRT Drivers
- Brake gently—passengers can fall.
- Test brakes at low speed first.
⚡ Forklift Operators
- Watch for air leaks (common in dusty environments).
- Park with spring brake engaged.

## Slide 22: Quiz
❓ Why should bus drivers avoid sudden braking?
A) To save fuel
B) To prevent passenger injuries ✅
C) To reduce air compressor wear
❓ What should you do FIRST if air brakes fail while driving?
A) Pull the emergency brake immediately
B) Pump the brake pedal to rebuild pressure ✅
C) Turn off the engine

## Slide 23: Key Safety Tips
Air brakes are powerful but require knowledge and maintenance. Whether you drive a school bus, forklift, or 18-wheeler, understanding these systems keeps everyone safe. Always inspect, always stay alert, and never ignore warning signs!
Air brakes require proper training and practice. Always follow CDL (Commercial Driver’s License) guidelines and FMCSA regulations when operating vehicles with air brakes.
✔ Air brakes take longer to stop than car brakes—allow extra distance.
✔ Never let pressure drop below 60 psi(spring brakes may engage).
✔ Daily maintenance is crucial—drain tanks, check hoses.
✔ If in doubt, get a professional inspection.
✔ Always perform a brake test before driving.
✔ Keep air tanks drained to prevent moisture buildup.
✔ If brakes fail, pump the pedal to build air pressure

## Slide 24: Quiz
❓ What is the minimum safe air pressure before driving?
A) 50 psi
B) 90 psi ✅
C) 150 psi
❓ True or False: Air brakes work the same way as car brakes.
False ✅ (Air brakes need pressure to release brakes)
❓ What engages automatically if air pressure drops too low?
A) Cruise control
B) Spring brakes ✅
C) Hazard lights