## Slide 1: Double Trailer Handout

## Slide 2: TABLE OF CONTENTS
1. Introduction to Double Trailers 2. Pre-Trip Inspection Guide 3. Coupling & Uncoupling 4. Driving Techniques 5. What to do in an emergency & Troubleshooting

## Slide 3: Introduction to Double Trailers
A double trailer (twin trailers, doubles, tandem trailers), is a truck that pulls two trailers at once. The first trailer is attached to the truck, and the second trailer is connected to the first one using something called a converter dolly — it’s like a small cart with wheels and a hitch.
Double trailers are used to haul more cargo in one trip. This saves time, fuel, and money. But driving them isn’t easy. They’re longer, harder to turn, and more likely to tip over if you're not careful.

## Slide 4: Introduction to Double Trailers
There are different types of Double Trailers, not all double trailers are the same.
The most common types in the U.S. are:
Rocky Mountain Doubles
  First trailer: 48-53 feet long.
  Second trailer: Shorter (28-40 feet).
  They are mostly used in Western states like Colorado and Utah in the USA.
Turnpike Doubles
  Both trailers: 28-48 feet each.
  Total length: Up to 110 feet.
  They are used on Toll roads ("turnpikes") and approved highways.
Standard Doubles (Pup Trailers)
  Both trailers: 28 feet each.
  They are common for General freight.

## Slide 5: Quiz
What connects the second trailer in a double trailer setup?
A coupling chain
A converter dolly
A tow bar
A rear axle
Why do drivers need to be extra careful when turning with double trailers?
They are easier to control
They take up more room
They don’t need mirrors
They speed up faster

## Slide 6: Quiz
What is another name for double trailers?
a) Single trailers
b) Twin trailers
c) Flatbeds
How many trailers does a double trailer setup have?
a) One
b) Two
c) Three
6. Double trailers are mainly used for:
a) Local deliveries
b) Long-haul freight
c) Passenger transport

## Slide 7: Quiz
Which country commonly uses double trailers?
a) Japan
b) USA
c) Germany
How long is each trailer in a standard "pup" double setup?
a) 53 feet
b) 28 feet
c) 40 feet

## Slide 8: Quiz
Which type of double trailer has one long and one short trailer?
a) Turnpike Double
b) Rocky Mountain Double
c) Pup Trailer
What should you always do before driving a double trailer?
Check equipment
Rev the engine
Honk the horn
Change the oil

## Slide 9: Quiz
True or False: The second trailer is attached directly to the truck.
a) True
b) False
True or False: Rocky Mountain Doubles are common in Florida.
a) True
b) False
Which type allows the longest combined trailer length?
a) Pup Trailers
b) Turnpike Doubles
c) Rocky Mountain Doubles

## Slide 10: Key Safely Tips
Always check your truck and trailers before driving.
Turn slowly and carefully — you need more space.
Avoid sudden stops or sharp turns.
Keep a longer distance between you and the vehicle ahead.
Watch for "cracking the whip" — the rear trailer can swing out wide if you drive too fast or turn too sharply

## Slide 11: Laws and Regulations
FMCSA = The U.S. government agency that regulates trucking safety.
Makes rules for truck drivers, trucking companies, and trailers.
Ensures trucks are safe to drive and drivers are properly trained.
Why Does FMCSA Care About Double Trailers?
Doubles are longer & harder to control than single trailers.
More risk of jackknifing, rollovers, and crashes if not driven safely.
FMCSA Rules for Drivers:
✔ Must have a CDL Class A (Commercial Driver’s License).
✔ Must have a "T" (Doubles/Triples) endorsement on the CDL.
✔ Must be at least 21 years old for interstate (crossing state lines).

## Slide 12: Laws and Regulations
Training Requirements:
Must pass a written test on doubles safety.
No extra road test, but training is highly recommended.
Safety & Inspection Rules
FMCSA Requires:
✔ Pre-Trip Inspection: Check hitches, brakes, tires, lights, and air lines.
✔ Secure Loads Properly: Unbalanced cargo = swaying or rollover risk.
✔ Follow Speed Limits: Often lower for doubles (e.g., 55-60 mph).

## Slide 13: Laws and Regulations
Double trailers improve freight efficiency but require proper training and safety measures. Laws vary by state, so drivers must follow regulations carefully. Understanding their types, laws, and risks is key for anyone in the trucking industry.
Federal Rules
Minimum driver age: 21 (for interstate driving).
Special license: CDL (Commercial Driver’s License) with a doubles/ triple's endorsement.
Weight limits: Vary by state (usually 80,000 lbs. max).
Route restrictions: Some states ban doubles on certain roads.
Allowed in: Most states, but with varying rules.
Banned in: Some states like New York (except on turnpikes).
Double trailers help move goods efficiently but require skilled drivers and strict safety measures.
Safety Concerns :Double trailers are harder to control than single trailers.

## Slide 14: Laws and Regulations
Common Risks
Jackknifing: Trailers swing out of control.
Rollovers: Higher center of gravity increases tipping risk.
Longer stopping distance: Takes more space to brake.
Safety Tips
✔ Proper training for drivers.
✔ Regular maintenance (tires, brakes, hitches).
✔ Avoid sharp turns & sudden stops.
FMCSA rules keep double trailer operations safe and legal. Always:
✔ Follow weight & length limits.
✔ Inspect your rig before driving.
✔ Know where doubles are allowed.

## Slide 15: Double Trailers CDL Class
CDL Classes
CDL Class A: Needed for double trailers (and most big rigs).
Covers tractor-trailers, semi-trucks, and doubles/triples.
Required if the combined weight is 26,001+ lbs. (with the trailer over 10,000 lbs.
CDL Class B: Only for single heavy trucks (no doubles).
CDL Class C: For small commercial vehicles (e.g., passenger vans, hazmat).
The "T" Endorsement
Even with a Class A CDL, you need a Doubles/Triples (T) endorsement to legally pull two or three trailers.
Without it, you can only drive a single trailer.

## Slide 16: Double Trailers CDL Class
How to Get the Doubles/Triples (T) Endorsement
Get a CDL Class A First:
Pass written general knowledge test.
Pass skills test (pre-trip inspection, basic control, road test).
Apply for the "T" Endorsement:
Study the doubles/triples section of your state’s CDL manual.
    Pass a written test (usually 20 questions).
    Pay the Fee ($25 / $50, varies by state).
    Get Your Updated CDL with the "T" endorsement.
No Extra Road Test Needed!
Unlike tanker (N) or hazmat (H), you don’t need a separate driving test for doubles.

## Slide 17: Where Can You Drive Doubles?
✔ Allowed: Most interstates & major highways (check state laws).
❌ Banned in: Some states (e.g., New York except turnpikes).
Speed Limits for Doubles
Often lower than single trailers (e.g., 55-60 mph in some states).
Weight Limits
Federal max: 80,000 lbs. (varies by state).
Getting a doubles/triples (T) endorsement is not hard, but driving doubles safely takes skill.
Always:
✔ Check state laws before driving.
✔ Practice in low-traffic areas first.
✔ Maintain proper speed & weight limits.

## Slide 18: Common Mistakes to Avoid
1. Skipping Practice
Doubles handle differently—practice in a safe area first.
2. Ignoring Weight Distribution
Uneven loads cause swaying or rollovers.
3. Taking Sharp Turns Too Fast
Doubles need wider turns—swing out to avoid hitting curbs.
4. Forgetting the "T" Endorsement
Driving doubles without it = big fines & license suspension.

## Slide 19: Pros and Cons of Double Trailers
Pros:
✅ More cargo per trip = fewer trucks on the road.
✅ Cost-effective for shipping companies.
✅ Better fuel efficiency per ton of freight.
Cons:
❌ Harder to drive & maneuver.
❌ Higher accident risk if not handled properly.
❌ Not allowed on all roads.

## Slide 20: Quiz
What license is needed to drive double trailers?
a) Regular driver’s license
b) CDL with doubles endorsement
c) Motorcycle license
The minimum age to drive doubles across state lines is:
a) 18
b) 21
c) 25
True or False: All U.S. states allow double trailers everywhere.
a) True
b) False

## Slide 21: Quiz
What is "jackknifing"?
a) Trailers folding like a pocket knife
b) A type of truck
c) A speed limit sign
Why do double trailers have a higher rollover risk?
a) They are shorter
b) Higher center of gravity
c) They are lighter
True or False: Double trailers stop faster than single trailers.
a) True
b) False

## Slide 22: Quiz
True or False: Double trailers are easier to drive than single trailers.
a) True
b) False
What is a disadvantage of doubles?
a) Better fuel efficiency
b) Not allowed everywhere
c) Fewer accidents
Which is NOT a pro of double trailers?
a) More cargo per trip
b) Higher accident risk
c) Cost savings

## Slide 23: Quiz
Which CDL class is required for double trailers?
a) Class B
b) Class A
c) Class C
A Class A CDL is required if the combined weight is over:
a) 10,000 lbs.
b) 26,001 lbs.
c) 50,000 lbs.
Can you drive triples with just a Class A CDL (no endorsements)?
a) Yes
b) No

## Slide 24: Quiz
Where can you study for the doubles test?
a) Your state’s CDL manual
b) A random trucking blog
c) YouTube comments
How much does the "T" endorsement usually cost?
a) $10
b) 25-25−50
c) $200
Can you get a "T" endorsement with a Class B CDL?
a) Yes
b) No

## Slide 25: Quiz
What must you check in a pre-trip inspection?
a) Hitches & brakes
b) Your lunchbox
c) The radio
True or False: Unbalanced loads are safe for doubles.
a) True
b) False
Why do doubles need slower speeds?
a) They stop faster
b) They need more stopping distance
c) Just for fun

## Slide 26: Quiz
True or False: You need a special road test for the "T" endorsement.
a) True
b) False
How old must you be to drive doubles across state lines?
a) 18
b) 21
c) 25
What should you do before driving doubles?
a) Just start driving
b) Get proper training
c) Ask a friend for tips

## Slide 27: Quiz
What does FMCSA stand for?
a) Federal Motor Carrier Safety Administration
b) Fast Moving Cars Safety Agency
c) Freight Management and Cargo Safety Authority
What is FMCSA’s main job?
a) Selling trucks
b) Regulating trucking safety
c) Building highways
True or False: FMCSA only cares about single trailers.
a) True
b) False

## Slide 28: Pre-Trip Inspection Guide
Pre-trip inspections are the most important 15 minutes of a trucker’s day.
Before a double trailer hits the road, drivers must perform a DVIR (Driver Vehicle Inspection Report)—a safety check that’s like a pilot’s pre-flight checklist.
Here’s what truckers inspect, why it matters, and how YOU could spot problems too!
Why Pre-Trip Inspections Save Lives
✅ Prevents breakdowns (A blown tire at 65 mph is deadly)
✅ Avoids 10,000 fines (DOT officers check inspection logs)
✅ Keeps cargo safe(Loose straps = spilled goods = big 10,000fines

## Slide 29: Pre-Trip Inspection Guide
The 7-Point Double Trailer Check (Drivers use the acronym "TIRES D" to remember)
1. T – Tires & Wheels
🔸 Tread depth: Must be >4/32" (Use a quarter upside-down!)
🔸 Pressure: Check with a gauge (100+ PSI for big rigs)
🔸 Damage: Look for bulges, cuts, or nails
🔸 Lug nuts: Must be tight (Mark them with chalk to check)
2. I – Lights & Reflectors 🔦 Test ALL lights:
● Headlights (low/high beam) ● Brake lights ● Turn signals
● Clearance lights (Top of trailer)
● Reflectors (Must be unbroken) "Blackout" Danger: Broken lights = invisible trailer at night

## Slide 30: Pre-Trip Inspection Guide
3. R – Rigging (Coupling System)
🔗 Fifth wheel: Locked? Greased? No cracks?
🛠 Dolly: Pintle hook secured? Safety chains attached?
🚛 Kingpin: Not worn down (Thieves steal these for scrap!)
Scary Fact: A "trailer breakaway" happens when coupling fails—the trailer rolls free!
4. E – Emergency Equipment
🧯 Fire extinguisher: Charged & mounted
⚠️ Reflective triangles/road flares: 3 required
📞 Emergency contacts: Posted in cab

## Slide 31: Pre-Trip Inspection Guide
5. S – Suspension & Frame
🛠 Springs/airbags: No leaks or damage
🔩 U-bolts: All present and tight
🚛 Frame: No cracks or rust holes
Watch For: A "dog walking" trailer (sways side-to-side if suspension fails)!
6. D – Doors & Cargo (If Loaded)
📦 Seals intact? (Broken = possible theft)
🔒 Locking pins engaged?
🧰 Cargo secured? (Straps, chains, or load bars tight)
Trucker Hack: Spray WD-40 on door hinges to stop freezing shut in winter!

## Slide 32: Key Points
Drivers must understand the interdependence of systems in double trailers.
Inspect the air brake system in detail: check the air compressor, reservoirs, brake chambers, and glad hands.
Perform a full brake test: air leakage test, applied pressure test, and emergency spring brake activation.
Look for signs of wear on suspension components such as leaf springs and torque arms.
Ensure all electrical connectors are secure and not corroded.

## Slide 33: Coupling and Uncoupling
Coupling (hooking up) and uncoupling (dropping) double trailers is one of the most critical skills for truckers. A mistake can lead to rollaway, damaged equipment, or even deadly accidents.
Coupling and uncoupling might seem simple, but one missed step can cause disaster. Professional drivers practice this until it’s second nature.
Here’s how professionals do it safely.

## Slide 34: Coupling and Uncoupling
🛠 Tools Needed
✅ Gloves (Grease and dirt protection)
✅ Dolly Handle (To move the dolly manually)
✅ Chock Blocks (To prevent rolling)
✅ Fifth Wheel Grease (Reduces friction)
✅ Flashlight (For night checks)

## Slide 35: COUPLING (Hooking Up)
Step 1: Park and Prepare
Position the tractor in line with the trailers.
Set parking brakes on both tractor and trailers.
Chock the wheels of both trailers (front and rear).
Step 2: Connect the First Trailer (Lead Trailer to Tractor)
1. Back the tractor slowly until the fifth wheel touches the trailer kingpin.
2. Check alignment – The kingpin should slide into the fifth wheel jaws.
3. Listen for the "CLUNK" – The locking mechanism should engage.
4. Tug test – Gently pull forward to confirm it’s locked.
5. Raise landing gear (if applicable).
Step 3: Connect the Dolly to the First Trailer
1. Position the dolly under the rear of the first trailer.
2. Lower the dolly legs to support it.

## Slide 36: COUPLING (Hooking Up)
3. Back the first trailer until the dolly’s pintle hook locks onto the trailer’s ring.
4. Secure safety chains (crossed under the connection).
Step 4: Connect the Second Trailer to the Dolly
1. Back the dolly into the second trailer’s kingpin.
2. Lock the jaws (same as Step 2).
3. Plug in light cords (test all lights!).
4. Raise dolly legs fully.
Step 5: Final Checks
✔ Tug test both trailers (no movement at connections).
✔ Check air lines (no leaks, brakes apply correctly).
✔ Verify all lights (turn signals, brake lights, clearance lights).

## Slide 37: UNCOUPLING (Dropping)
Step 1: Park Safely
● Find level ground (prevents rolling).
● Set parking brakes on tractor and both trailers.
● Chock all wheels (front and rear of both trailers).
Step 2: Disconnect the Second Trailer from the Dolly
1. Lower dolly legs until they touch the ground.
2. Disconnect light cords and air lines.
3. Pull the fifth wheel release handle.
4. Slowly pull forward to separate.
Step 3: Disconnect the Dolly from the First Trailer
1. Lower landing gear on the first trailer.
2. Unhook safety chains.

## Slide 38: UNCOUPLING (Dropping)
3. Pull the pintle hook release lever.
4. Drive forward to separate.
Step 4: Disconnect the First Trailer from the Tractor
1. Lower landing gear (if not already down).
2. Disconnect air and electrical lines.
3. Pull the fifth wheel release handle.
4. Drive forward slowly to detach.
Step 5: Secure Everything
✔ Make sure trailers are stable (landing gear fully down).
✔ Chock wheels again (prevents rolling).
✔ Store air lines and cords properly (no tangles).

## Slide 39: UNCOUPLING (Dropping)
⚠️ COMMON MISTAKES (And How to Avoid Them)
❌ Forgetting to chock wheels → Trailer rolls away!
❌ Not doing a tug test → Trailer detaches on the highway!
❌ Leaving dolly legs up → Dolly crashes into trailer!
❌ Ignoring air leaks → Brakes fail!

## Slide 40: Advanced Coupling/Uncoupling Techniques
Cold Weather Considerations
❄️Fifth Wheel Freeze Prevention:
● Apply graphite grease (not oil-based, which attracts dirt)
● Keep lock jaws de-iced with alcohol spray
● Test pull twice - thermal contraction can cause false locks
Night Operation Protocol
🔦 Lighting Checklist:
1. Headlamp on trailer kingpin area
2. Glow sticks on dolly legs (when lowering)
3. Headlamp strap for hands-free inspection
Weight Distribution Math
⚖️ Ideal Loading Formula:
● Lead trailer: 60% of total cargo weight
● Rear trailer: 40% of total cargo weight
● Dolly weight: Must be included in bridge formula calculations
Example: For 80,000 lb. GCW:
● Lead trailer = 48,000 lbs.
● Rear trailer = 32,000 lbs.

## Slide 41: Quiz
What’s the FIRST thing you do before coupling?
Grease the fifth wheel
Set parking brakes and chock wheels
Honk the horn
Why do you cross the safety chains under the dolly?
To catch the trailer if it detaches
It looks cooler
Because the DOT says so
3. What’s the “tug test”?
Checking if the trailer is too heavy
Pulling gently to confirm the fifth wheel is locked
Yanking the steering wheel to test handling

## Slide 42: Driving Techniques for Double Trailers
Mastering the Road Driving a double trailer (also called "pulling doubles" or "tandem trailers") requires precision, patience, and special skills that go beyond standard trucking.
Here’s a breakdown of key techniques every professional uses to stay safe on the road.
🚛 Key Differences from Single-Trailer Driving
✅ Longer stopping distance (Up to 40% more space needed!)
✅ Wider turns required (Or risk "off-tracking" into other lanes)
✅ More sway risk (Wind, uneven roads, or sudden moves can cause fishtailing)
✅ No easy reversing (Most doubles cannot back up without uncoupling)

## Slide 43: Driving Techniques for Double Trailers
🛣 Essential Driving Techniques
1. Steering & Lane Control
🔹 Stay centered in your lane – Doubles take up more space.
🔹 Avoid sudden movements – Smooth steering prevents trailer sway.
🔹 Use both mirrors constantly – The second trailer swings wider than you think!
Pro Tip: If the trailer starts swaying, do NOT brake hard—ease off the gas and steer gently
2. Turning Correctly
🔄 Wide right turns – Swing left first to avoid curbing the dolly.
🔄 Extra space for left turns – The second trailer "off-tracks" behind you.
🚦 Never turn on red unless 100% sure – You need two gaps in traffic!
Danger Zone: A tight turn can cause a "jackknife" (trailer folds toward the cab).

## Slide 44: Driving Techniques for Double Trailers
3. Braking & Downhill Control
🛑 Brake early – Doubles need 2x more stopping distance.
⏬ Use engine braking ("Jake Brake") on steep hills to avoid overheating brakes.
⚠️ Never "ride the brakes" – They can fade or catch fire from overheating.
Did You Know? Some mountain roads ban doubles because of steep grades.
4. Managing Sway & Wind
💨 Crosswinds? Grip the wheel firmly and steer slightly into the wind.
🌀 Trailer fishtailing? Ease off the gas—never jerk the wheel!
🌧 Wet roads? Slow down 5-10 mph below the limit.
Trucker Trick: Keep half a tank of fuel in front for better weight balance.

## Slide 45: Driving Techniques for Double Trailers
5. Passing & Being Passed
🚗 Passing others: Only if you have clear space for 2+ trailers ahead.
🚛 Being passed: Stay right, avoid speeding up, and watch for tail swing.
🚫 No "elephant races"! (Don’t block lanes trying to pass another slow truck.
️ High-Risk Situations & How to Handle Them
Emergency Stopping
● Pump brakes (if no ABS) to avoid locking wheels.
● Use escape ramps if brakes fail on a hill.
2. Tire Blowout
● Do NOT slam brakes!
● Grip wheel tightly and coast to a safe stop.
3. Avoiding Rollovers
● Take curves 5 mph slower than posted speed.
● Watch for "rollover risk" signs on highway ramps.

## Slide 46: Quiz
What should you do if your double trailer starts swaying?
Ease off the gas and steer gently
Slam on the brakes
Speed up to stabilize
2. Why should you swing left before a right turn?
To check your blind spot
To avoid running the dolly over the curb
Because it confuses other drivers
3. True or False: Doubles can reverse easily like single trailers.

## Slide 47: Troubleshooting & Emergency Handling
Driving double trailers comes with unique risks—from trailer sway to brake failures.
Knowing how to react calmly and correctly can mean the difference between a close call and a catastrophe.
Here’s your emergency playbook.

## Slide 48: What to Do in an Emergency
⚠️ COMMON EMERGENCIES & HOW TO HANDLE THEM
1. Trailer Sway (Fishtailing)
Causes: Crosswinds, uneven loading, sudden steering.
What to do:
✔ Ease off the accelerator (DO NOT brake hard!)
✔ Steer gently into the sway (If trailer swings left, steer left)
✔ Activate trailer brakes only (If equipped with independent control)
🚫 Never jerk the wheel or panic brake—it worsens sway!
Prevention:
● Balance cargo weight (60% front, 40% rear trailer).
● Avoid overcorrecting steering.

## Slide 49: What to Do in an Emergency
2. Tire Blowout What it feels like: Loud bang + steering pull.
What to do:
✔ Firm grip on the wheel (Expect a strong pull)
✔ Do NOT slam brakes (Causes loss of control)
✔ Let off gas, coast to safety
✔ Use 4-ways (hazards) and exit highway if possible
Prevention:
● Pre-trip tire checks (look for cracks, bulges).
● Maintain proper PSI (check when cold).

## Slide 50: What to Do in an Emergency
3. Brake Failure Signs: Pedal goes soft, truck isn’t slowing.
What to do:
✔ Pump brakes (If non-ABS)
✔ Downshift (Use engine braking)
✔ Use emergency/parking brake gradually
✔ Find an escape ramp or open space
Last Resort:
● Rub against guardrails or berms to slow down (controlled friction).

## Slide 51: What to Do in an Emergency
4. Jackknife (Trailer Folds Toward Cab)
Causes: Braking too hard in a turn, icy roads.
What to do:
✔ Release brakes immediately
✔ Steer toward the skid (If trailer swings left, steer left)
✔ Avoid overcorrecting (Small steering inputs only)
Prevention:
● Slow down before curves.
● Brake before turning, not during.

## Slide 52: What to Do in an Emergency
5. Rollaway (Trailer Detaches or Rolls Uncontrolled)
Causes: Failed fifth wheel, improper uncoupling.
What to do:
✔ Stay in cab—DO NOT chase it!
✔ Use CB radio to warn others (“Runaway trailer on I-80 westbound!”)
✔ Call 911 immediately
Prevention:
● Always chock wheels before uncoupling.
● Double-check fifth wheel lock.

## Slide 53: What to Do in an Emergency (Extreme Scenario Protocols )
Blowout at Speed
💥 Controlled Response:
1. Grip wheel at 10 & 2 (expect 300+ lb pull)
2. Count "one-one thousand" before reacting
3. Gradual lane change - no more than 3° steering input

## Slide 54: What to Do in an Emergency (Extreme Scenario Protocols )
Hydroplane Recovery
🌊 3-Phase Technique:
1. Feather throttle (no acceleration/deceleration)
2. Look where you want to go (not at obstacles)
3. Wait for tread contact before gentle corrections
Terrorist Stop (Forced Brake Check)

## Slide 55: What to Do in an Emergency (Extreme Scenario Protocols )
🚨 Defensive Maneuver:
● Progressive brake squeeze (20% pressure increments)
● Trailer brake priority if equipped with separate control
● Horn blast sequence (3 short, 2 long) to alert others

## Slide 56: What to Do in an Emergency (Troubleshooting Common issues)
Problem | Quick Fix
Air pressure warning | Pull over, check for leaks, rebuild pressure.
Dolly won’t lock | Clean kingpin, check jaws, grease fifth wheel.
Electrical failure (no trailer lights) | Check fuses, connections, ground wire.
Refrigerated trailer warming up | Check fuel, thermostat, door seals.
Suspension sagging | Stop driving—could indicate broken airbag/spring.

## Slide 57: What to Do in an Emergency (Air System Fault Diagnosis)
Problem | Likely cause | Fix
Rapid pressure drop | Gladhand seal failure | Carry spare seals
Brakes slow to release | Clogged airline | Blow out with 100 psi
Trailer brakes lock | Frozen brake chamber | Alcohol squirt bottle

## Slide 58: What to Do in an Emergency (Electrical Ghost Problems)
🔌 Test Sequence:
1. Check ground connection (50% of faults)
2. Test pigtail continuity with multimeter
3. Inspect relay module for corrosion

## Slide 59: What to Do in an Emergency
📞 EMERGENCY CONTACTS TO KNOW
● State DOT Helpline (Posted on highway signs)
● Company Safety Dept. (Keep number in cab)
● Roadside Assistance (e.g., AAA for trucks)
Pro Tip: Program these into your phone before a crisis!

## Slide 60: What to Do in an Emergency
Emergency Kit Must-Haves 🛠
Professional-Grade Load:
● Air line repair kit (with brass fittings)
● 5-ton bottle jack (regular jacks will collapse)
● Folding wheel chocks (aluminum, not plastic)
● Glow stick flares (last 12 hours, safer than flames)
● Kingpin lock (theft prevention during stops)

## Slide 61: What to Do in an Emergency
Regulatory Hotspots Weigh Station Bypass Logic
⚖️ PrePass Decision Tree:
● Green light? Check dashboard confirmation light
● Red light? Pull in even if scale looks closed
● No PrePass? Weigh every 250 miles
ELD Exceptions Cheat Sheet
⏱️ Legal Exemptions:
● First 100 air miles (short-haul exception)
● Agricultural commodities (150-air-mile radius)
● Oilfield operations (wait time doesn't count)

## Slide 62: Quiz
Scenario 1: Your second trailer starts swaying violently in wind. Do you:
a) Ease off gas, steer gently into it
b) Slam brakes to slow down
c) Speed up to stabilize
Scenario 2: Brake pedal sinks to the floor on a downhill. Next move?
a) Downshift + use Jake Brake
b) Pull steering wheel hard left
c) Text your dispatcher

## Slide 63: Quiz
Scenario 3: You see sparks from a trailer wheel. Action?
a) Ignore it—it’ll stop soon
b) Pull over ASAP—wheel bearing may be failing
c) Throw water on it

## Slide 64: Key Points
💡 FINAL TIP: PRACTICE MAKES PERFECT
New drivers should simulate emergencies in empty lots:
● Practice controlled skid recovery
● Test brake failure responses
● Master trailer sway control
Remember: In an emergency, stay calm, act early, and prioritize safety over speed.
🚛 Now you’re prepared for the worst—drive safe out there!
(Bonus: Ask experienced drivers about their wildest roadside fixes—duct tape and bungee cords work miracles!) 🛠😄