## Slide 1: Truck Driving Essentials
General Knowledge, Air Brakes, Combination Vehicles, Hazmat, Pre-Trip & Post-Trip Inspections

## Slide 2: 1. General Knowledge

## Slide 3: 1.A Introduction to Truck Driving
Truck driving is a crucial part of the transportation industry, responsible for moving goods across cities, states, and countries. To become a professional truck driver, you must obtain a Commercial Driver’s License (CDL) and follow strict safety regulations.

## Slide 4: 1.B CDL License Types
Class A: Allows you to drive combination vehicles with a gross vehicle weight rating (GVWR) of 26,001 lbs. or more and tow trailers over 10,000 lbs. (e.g., tractor-trailers)
Class B: For straight trucks and buses, GVWR of 26,001 lbs. or more, but towing is limited to 10,000 lbs. or less.
Class C: For vehicles transporting hazardous materials (Hazmat) or 16+ passengers (including the driver).

## Slide 5: 1.C Types of Trucking Jobs
• Local Trucking – Short-distance deliveries, usually within a city or state.
• Regional Trucking – Transporting goods within a specific region, covering multiple states.
• Over-the-Road (OTR) Trucking – Long-distance transportation across the country.
• Hazmat Trucking – Specialized transportation of hazardous materials, requiring extra safety training.

## Slide 6: 1.1 Basic Vehicle Controls
Driving a truck requires mastering basic vehicle controls to ensure safety and efficiency.
Steering: Always keep both hands on the wheel at the 9 and 3 o’clock positions to maintain full control. Avoid sudden steering movements, as trucks are large and heavy, making abrupt turns dangerous.
Braking: Trucks have multiple braking systems:
Service Brakes: Used during normal driving.
Emergency Brakes: Engage when air pressure drops too low.
Parking Brakes: Used when the truck is stopped to prevent rolling.
Acceleration: Trucks take longer to speed up compared to regular vehicles. Gradual acceleration prevents cargo from shifting and maintains fuel efficiency.
Shifting Gears: Manual transmissions require smooth gear shifting to prevent transmission damage. Automatic trucks adjust gears automatically, but the driver should still monitor RPMs and road conditions.

## Slide 7: 1.2 Defensive Driving
Defensive driving techniques help prevent accidents and keep drivers safe.
Space Management:
Maintain at least 7-8 seconds following distance to allow for braking time.
Be extra cautious in heavy traffic, construction zones, or bad weather.
Looking Ahead:
Scan the road 12-15 seconds ahead to anticipate potential hazards.
Identify slow-moving vehicles, road debris, or sudden stops early.

## Slide 8: 1.2 Defensive Driving(contd)
Blind Spots (“No-Zones”):
Trucks have large blind spots on the sides, rear, and front.
Avoid driving directly beside or behind another vehicle for long periods.
Lane Changes:
Use mirrors frequently and signal well in advance.
Change lanes gradually to avoid sudden movements.
Speed Control:
Adjust speed according to road, traffic, and weather conditions.
Avoid excessive speeds, especially on curves and downhill sections.

## Slide 9: 1.3 Road Signs and Rules
Understanding road signs and traffic laws is crucial for safe truck driving.
Regulatory Signs:
Speed limits, lane usage, weight restrictions, and truck routes must be obeyed.
Warning Signs:
Indicate curves, steep grades, narrow bridges, and construction zones.
Right of Way:
Always yield to emergency vehicles and pedestrians.
Understand four-way stop and intersection rules.
Railroad Crossings:
Always slow down and check for trains.
Stop 15-50 feet before tracks when required.

## Slide 10: 1.4 Cargo Securement
Ensuring cargo is properly secured prevents accidents and damage.
Weight Limits:
Stay within legal weight limits for axles and overall gross weight.
Load Distribution:
Cargo must be evenly distributed to prevent shifting.
Tie Downs and Straps:
Use appropriate chains, straps, or tarps to keep loads stable.
Hazardous Materials (Hazmat):
Follow DOT regulations for labeling, placarding, and handling dangerous goods.

## Slide 11: 1.5 Weather and Road Conditions
Adjusting driving techniques for different weather conditions is essential.
Rain:
Increase following distance.
Avoid sudden braking to prevent skidding.
Snow/Ice:
Use tire chains when required.
Reduce speed and avoid sudden movements.
Fog:
Use low-beam headlights.
Drive at a slower speed for better reaction time.
High Winds:
Be cautious on bridges and open roads.

## Slide 12: 1.6 Night Driving
Driving at night requires extra precautions.
Use High Beams Wisely:
Only when necessary; dim for oncoming traffic.
Clean Lights and Reflectors:
Keep headlights, taillights, and mirrors clean for maximum visibility.
Watch for Fatigue:
Take breaks every 2-3 hours.
Avoid driving if feeling drowsy.

## Slide 13: 1.7 Driving Emergencies
Handling emergencies correctly can prevent accidents.
Brake Failure:
Use the emergency brake and downshift to slow down.
Tire Blowout:
Hold the steering wheel firmly and let the truck slow down gradually.
Jackknifing:
Release brakes and steer gently to straighten the trailer.
Engine Fire:
Shut off the engine and use a fire extinguisher if safe.

## Slide 14: 1.8 Accident Procedures
If an accident occurs, follow these steps:
Stop Immediately – Move to a safe location if possible.
Secure the Scene – Use warning triangles or flares.
Call for Help – Contact law enforcement and emergency services.
Exchange Information – Share license, insurance, and contact details.

## Slide 15: 1.9 Hours of Service (HOS) Regulations
Federal laws regulate driving hours to prevent fatigue.
11-hour driving limit – Drive maximum 11 hours after 10 consecutive hours off-duty.
14-hour limit – Cannot drive beyond 14 consecutive hours.
30-minute break – Required after 8 hours of driving.
60/70-hour limit – Cannot drive more than 60 hours in 7 days or 70 hours in 8 days.

## Slide 16: 1.10 Vehicle Maintenance
Regular maintenance keeps the truck in good condition.
Daily Inspections: Check fluids, tires, brakes, and lights.
Oil Changes: Follow the truck’s maintenance schedule.
Brake System Maintenance: Ensure air pressure is within safe levels.

## Slide 17: 1.11 Fuel Efficiency
Saving fuel reduces costs and environmental impact.
Idle Reduction: Turn off the engine when not in use.
Smooth Driving: Avoid rapid acceleration and braking.
Proper Tire Inflation: Maintain correct pressure to improve fuel economy.

## Slide 18: 1.12 Communication on the Road
CB Radio: Useful for communicating road conditions with other truckers.
Hand Signals: Use when backing up with a spotter.

## Slide 19: 1.12.1 Basic Hand Signals for Truck Drivers
These signals help ensure safe maneuvering, particularly when backing up or parking.
Action | Hand Signal
Stop | Raise one hand, palm facing outward (like a “halt” signal).
Go Forward | Wave one hand in a forward motion, palm facing outward.
Turn Left | Extend left arm straight out.
Turn Right | Extend left arm and bend elbow upward at a 90-degree angle (L-shape).
Slow Down | Move hand up and down with palm facing downward.
Speed Up | Move hand up and down with palm facing upward.
Back Up | Make circular motions with both hands, palms facing inward (toward your body).
Move Left or Right | Point in the direction the vehicle should go.
All Clear | Raise both hands and give a thumbs-up.

## Slide 20: 1.12.2 Backing Up with a Spotter
Always agree on signals with the spotter before starting.
The spotter should stand where the driver can see them at all times.
If the driver loses sight of the spotter, they should stop immediately.
The spotter should use clear, exaggerated hand movements to avoid confusion.

## Slide 21: 1.12.3 Emergency and Roadside Signals
Emergency stop: Extend one arm straight up and move it in a circular motion.
Breakdown warning: Wave both arms overhead to signal to other drivers.
Would you like illustrations or more details on using hand signals effectively in different situations?
Flashing Lights: Signal other drivers when necessary.

## Slide 22: 1.13 Parking and Backing
Backing Up: Always check mirrors and use a spotter if possible.
Docking: Align properly with loading docks.
Parking Brakes: Always engage when stopped.

## Slide 23: 2 Air Brakes

## Slide 24: 2.1 Understanding Air Brakes
Air brakes are a critical component in heavy-duty vehicles, utilizing compressed air to activate the braking mechanism. This system is favored in commercial trucks due to its reliability and ability to maintain braking power even with minor leaks.

## Slide 25: 2.2 Key Components and Their Functions
Air Compressor
Function: Generates and supplies compressed air to the brake system.
Operation: Typically engine-driven, ensuring a continuous supply of air.
Maintenance Example: Regularly inspect for oil leaks and ensure the compressor is building pressure within the manufacturer's specified time frame.
Air Storage Tanks (Reservoirs)
Function: Store compressed air for immediate use during braking.
Safety Feature: Equipped with drain valves to remove accumulated moisture and oil.
Maintenance Example: Drain the tanks daily to prevent water accumulation, especially in humid conditions, to avoid brake failure due to freezing.

## Slide 26: Key Components and Their Functions(contd)
Brake Chambers
Function: Convert air pressure into mechanical force to apply the brakes.
Operation: Air pressure pushes a diaphragm, moving the pushrod to engage the brakes.
Inspection Example: Check for audible air leaks around the chamber and ensure the pushrod moves freely without obstruction.
Slack Adjusters and Pushrods
Function: Maintain the correct distance between brake shoes and drums, ensuring effective braking.
Adjustment Example: During inspections, pull the slack adjuster by hand; it should not move more than approximately one inch. Excessive movement indicates the need for adjustment.
Brake Shoes and Drums
Function: Create the friction necessary to slow down or stop the vehicle.
Wear Indicator Example: Regularly inspect brake shoes for wear; thin linings can lead to reduced braking efficiency and should be replaced promptly.
.

## Slide 27: 2.3 Air Brake System Operation
Applying the Brakes: Pressing the brake pedal increases air pressure in the brake chambers, pushing the diaphragm and activating the brakes.
Releasing the Brakes: Releasing the pedal decreases air pressure, allowing return springs to disengage the brakes.
Emergency Braking: In case of significant air loss, spring brakes automatically engage to stop the vehicle.

## Slide 28: 2.4 Inspections and Tests
Air Leakage Test
Procedure: With the engine off and air pressure built up, fully apply the foot brake and monitor the air pressure gauge.
Acceptable Loss: Should not exceed 3 psi per minute for single vehicles or 4 psi per minute for combination vehicles.
Compressor Cut-In/Cut-Out Test
Cut-Out Pressure: Compressor should stop pumping at approximately 125 psi.
Cut-In Pressure: Compressor should resume pumping at around 100 psi or as specified by the manufacturer.

## Slide 29: Inspections and Tests
Low-Air Pressure Warning Test
Procedure: With the engine running, slowly pump the brake pedal to reduce air pressure.
Warning Activation: A warning signal (light or buzzer) must activate before pressure drops below 60 psi.
Spring Brake Test
Procedure: Continue to pump the brake pedal after the low-pressure warning activates.
Activation: Parking brakes should engage automatically when pressure falls to the manufacturer's specified range, typically between 20-45 psi.
Service Brake Test
Procedure: Move the vehicle forward slowly and apply the brakes to ensure they function correctly without pulling to one side or delayed engagement.

## Slide 30: 2.5 Common Issues and Preventive Measures
Brake Fade: Occurs due to overheating from excessive use, leading to reduced braking power.
Prevention Example: Use engine braking on long descents and avoid continuous brake application.
Moisture Accumulation: Water in the system can cause corrosion and freezing.
Prevention Example: Regularly drain air tanks, especially in cold weather, to prevent ice formation that could block air flow.
Air Leaks: Can lead to insufficient air pressure for effective braking.
Detection Example: Listen for hissing sounds during inspections and use soapy water to identify leak points.

## Slide 31: 3 Combination Vehicles

## Slide 32: 3.1 Coupling and Uncoupling Procedures
Proper coupling and uncoupling of tractor-trailers are vital for safe operations. Incorrect procedures can lead to accidents, equipment damage, or cargo loss.

## Slide 33: Coupling and Uncoupling Procedures
Coupling Procedure:
1. Inspect Fifth Wheel:
Ensure the fifth wheel is securely mounted, undamaged, and properly lubricated. Verify that the jaws are open and the locking mechanism is functional.
2. Inspect Trailer Kingpin and Area:
Check the trailer kingpin for damage or excessive wear. Ensure the area around the trailer is clear of obstacles.
3. Position Tractor:
Align the tractor directly in front of the trailer. Back up slowly, centering the kingpin with the fifth wheel. Stop just before contact.
4. Secure Trailer:
Engage the trailer brakes to prevent movement during coupling.

## Slide 34: Coupling and Uncoupling Procedures
5. Back Under Trailer:
Using the lowest reverse gear, back the tractor slowly under the trailer to avoid hitting the kingpin too hard. Stop when the kingpin is locked into the fifth wheel.
6. Check Connection Security:
Perform a tug test by gently pulling forward with the trailer brakes engaged to ensure the fifth wheel jaws have locked onto the kingpin securely.
7. Connect Air and Electrical Lines:
Attach the service and emergency air lines and the electrical cable between the tractor and trailer. Ensure all connections are secure and free from damage.
8. Raise Landing Gear:
Fully retract the landing gear to prevent damage during transit.
9. Final Inspection:
Walk around the vehicle to verify all connections are secure, lights are functioning, and there are no visible issues.

## Slide 35: Coupling and Uncoupling Procedures
Uncoupling Procedure:
1. Position Vehicle:
Park on level ground and apply both tractor and trailer parking brakes.
2. Lower Landing Gear:
Extend the landing gear until it makes firm contact with the ground. In low gear, turn the crank a few extra times to lift some weight off the tractor.
3. Disconnect Air and Electrical Lines:
Detach the air lines and electrical cable, securing them to the tractor to prevent damage.

## Slide 36: Coupling and Uncoupling Procedures
4. Unlock Fifth Wheel:
Pull the fifth wheel release handle to disengage the locking mechanism.
5. Pull Tractor Forward:
Slowly move the tractor forward until the fifth wheel is clear of the trailer kingpin.
6. Secure Tractor:
Apply the tractor parking brake and conduct a final inspection to ensure the trailer is stable and the area is clear.

## Slide 37: Coupling and Uncoupling Procedures
Safety Tips
Consistency: Always follow a standardized procedure to minimize errors.
Awareness: Be mindful of your surroundings, especially in crowded or confined spaces.
Training: Regularly review and practice coupling and uncoupling techniques to maintain proficiency.

## Slide 38: 4 Understanding Hazmat (Hazardous Materials) in Truck Driving

## Slide 39: 4.1 What is Hazmat?
Hazmat stands for Hazardous Materials, which are substances that can pose a risk to health, safety, and the environment. Truck drivers must undergo special training and certification to transport hazmat safely.

## Slide 40: 4.2 Classes of Hazmat
Class | Hazmat Type | Examples
1 | Explosives | Fireworks, Ammunition
2 | Gases | Propane, Oxygen Tanks
3 | Flammable Liquids | Gasoline, Diesel, Paint Thinners
4 | Flammable Solids | Matches, Magnesium
5 | Oxidizing Substances | Bleach, Hydrogen Peroxide
6 | Toxic & Infectious Substances | Pesticides, Medical Waste
7 | Radioactive Materials | Uranium, Nuclear Medicine
8 | Corrosive Substances | Battery Acid, Drain Cleaner
9 | Miscellaneous Dangerous Goods | Lithium Batteries, Dry Ice

## Slide 41: 4.3 Rules for Transporting Hazmat Loads
1. Hazmat Endorsement – Drivers must pass a Hazmat Endorsement Test to obtain a special license.
2. Proper Labeling – All hazmat shipments must have correct labels and placards on the truck.
3. Securing the Load – Hazardous materials must be properly secured to prevent leaks or spills.
4. Emergency Response Plan – Drivers must know what to do in case of an accident involving hazmat.
5. Route Restrictions – Some roads and tunnels restrict hazmat transport, requiring drivers to plan alternative routes.
6. Documentation – Truckers must carry proper paperwork, including a Material Safety Data Sheet (MSDS), with details about the hazardous cargo.
7. Regular Vehicle Inspections – Hazmat trucks must be in top condition to prevent accidents.

## Slide 42: 5. Pre-Trip Inspection

## Slide 43: 5.1 What is a Pre-Trip Inspection?
A pre-trip inspection is a mandatory vehicle check before starting a trip to ensure the truck is safe and roadworthy. The inspection prevents mechanical failures and ensures compliance with Department of Transportation (DOT) regulations.

## Slide 44: 5.2 Steps for a Proper Pre-Trip Inspection
1. Check the Engine Compartment – Inspect oil, coolant, and transmission fluid levels.
2. Examine the Tires & Wheels – Ensure proper inflation and no visible damage.
3. Test the Brakes – Ensure brake pads and air brake system are working properly.
4. Inspect Lights & Signals – Test headlights, brake lights, and turn signals.
5. Check the Suspension System – Look for broken leaf springs and shocks.
6. Verify the Steering System – Ensure the steering wheel is responsive.
7. Inspect the Fuel System – Check for leaks and secure the fuel cap.
8. Check the Trailer Coupling System – Ensure the fifth wheel is properly latched.
9. Examine the Cargo Area – Ensure cargo is properly loaded and secured.

## Slide 45: 5.3 Why is a Pre-Trip Inspection Important?
• Ensures safety by preventing breakdowns.
• Helps drivers comply with DOT regulations.
• Saves money by reducing costly repairs.
• Prevents accidents due to mechanical failures.

## Slide 46: 6. Post-Trip Inspection

## Slide 47: 6.1 What is a Post-Trip Inspection?
A post-trip inspection is performed after completing a trip to identify any mechanical issues that need fixing before the next trip.

## Slide 48: 6.2 Key Steps in a Post-Trip Inspection
1. Check for Mechanical Issues – Inspect brakes, tires, and lights for any damage after the trip.
2. Inspect the Cargo Area – Ensure all goods were delivered safely without leaks or spills.
3. Look for Fluid Leaks – Check under the truck for any fuel, oil, or coolant leaks.
4. Test the Brakes Again – Ensure the braking system is still functioning properly.
5. Fill Out a Driver Vehicle Inspection Report (DVIR) – Document any defects or issues.

## Slide 49: 6.3 Why is a Post-Trip Inspection Important?
• Helps catch minor issues before they become major problems.
• Ensures the truck is ready for the next trip.
• Prevents compliance violations and penalties.

## Slide 50: Final Thoughts on Safe Truck Driving
By mastering Hazmat handling, Pre-Trip, and Post-Trip Inspections, drivers can ensure:
✅ Safety on the road
✅ Compliance with regulations
✅ Fewer breakdowns and costly repairs
✅ Successful deliveries and job security